## Slide 1
10. Satellite Communication & Radar Sensors
8e Applied EM by Ulaby and Ravaioli

## Slide 2
Overview

## Slide 3
Geosynchronous Satellites
To remain in sync with Earth’s rotation, a satellite has to be at an orbital altitude of 35,786 km above the Earth’s equator.
Three geosynchronous satellites are sufficient to cover the entire globe (up to 81◦ of latitude on either side of the equator).

## Slide 4
Geosynchronous Orbit
Gravitational force
(attractive)
Centrifugal force
(repulsive)
Equating them leads to:
Setting T = 23 hours, 56 minutes, and 4.1 seconds, and subtracting 6,378 km for Earth’s mean radius at the equator gives an altitude of h = 35, 786 km above Earth’s surface.
Notes: 4

## Slide 5
Frequency Bands

## Slide 6
Duplexers
A duplexer is used to separate the path of the received signal from that of the transmitted signal, thereby making it possible to connect a single antenna to the transmitter and receiver simultaneously.
A ferrite circulator is an example of a duplexer; its ferrite material allows waves to travel in only the clockwise direction.

## Slide 7
Transponder
A transponder receives an incoming signal (or many signals each occupying a certain bandwidth), amplifies it, changes its carrier frequency, divides the spectrum into channels, amplifies each channel with a high power amplifier, combines all channels and then transmits the full spectrum to the intended destination.
In this example, available bandwidth is 432 MHz, which can accommodate 75-100 TV Channels

## Slide 8
Communication-Link Power Budget
The signal-to-noise ratio is defined as the ratio of the signal power to the noise power at the input of an equivalent noise-free receiver
input power at the receiver with atmospheric losses taken into account
one-way transmissivity of the atmosphere at zenith angle θ

## Slide 9
Antenna Beams
Antenna feed arrays are used to shape the satellite antenna beam to suit the intended coverage

## Slide 10
Radar Sensors
The term radar is a contracted form of the phrase radio detection and ranging, which conveys some, but not all, of the features of a modern radar system

## Slide 11
Unambiguous Range
The range Ru corresponds to the maximum range that a target
can have such that its echo is received before the transmission
of the next pulse.

## Slide 12
Range Resolution
The range resolution of the radar, ∆R, is defined as the
minimum spacing between two targets necessary to avoid
overlap between the echoes from the two targets.
For a pulse length of 1 ns,
the range resolution is 15 cm

## Slide 13
Azimuth Resolution

## Slide 14
The Problem with Noise
For threshold detection level 1 indicated in Fig. 10-13, the radar will produce the presence of both targets, but it will also detect a false alarm. The chance of this occurring is called the false-alarm probability. On the other hand, if the threshold detection level is raised to level 2 to avoid the false alarm, the radar will not detect the presence of the first target. A radar’s ability to detect the presence of a target is characterized by a detection probability.

## Slide 15
Maximum Detectable Range
Through probability calculations, one can specify the minimum signal-to-noise ratio Smin required to assure a desired probability of detection.
The corresponding maximum detectable range is:
t = radar cross section of target
K = Boltzmann’s constant
Tsys = system noise temperature of receiver

## Slide 16
Doppler Effect

## Slide 17
Doppler Radar
Frequency of received signal
Frequency of transmitted signal
Doppler frequency shift

## Slide 18
Doppler Frequency

## Slide 19
Monopulse Radar
On the basis of information extracted from the echo due to
a single pulse, a monopulse radar can track the direction of a target with an angular accuracy equal to a fraction of its antenna beamwidth.
The phasing network is used to combine the backscattered signal in various ways so as to enhance vertical and horizontal resolutions.

## Slide 20
Monopulse Basic Concept

## Slide 21
Summary